## Slide 1
Fresh, Frozen or
Reconstituted Lyophilized Serum
Add alcoholic KOH solution
Hydrolysis
Sample Extraction
Place samples in water bath at 25 oC
Dry organic layer under nitrogen
Transfer organic layer to a new culture tube
Add Liebermann-Burchard reagent to each sample tube every 30 seconds and place in water bath at 25 oC
Spectrophotometry Analysis at 30 min
Data Processing and Results
Add hexane and DI water to perform liquid-liquid extraction
Thaw and mix on hematology mixer
Supplemental Figure 1S. Schematic representation of total cholesterol Abell Kendall RMP
Cooper GR et al., Clin. Chem., 1986, 32, 921-929

## Slide 2
Supplemental Figure 2S. Schematic representation of total glycerides RMP
Fresh, Frozen or
Reconstituted Lyophilized Serum
Dilute serum with Tris-HCl buffer solution
Add internal standard and alcoholic KOH solution
Hydrolysis
Sample Evaporation
Add derivatizing agent (pyridine and acetic anhydride mixture)
Derivatization
Extraction #2 and #3
with sodium bicarbonate
Extraction #4
with water
Centrifugation of serum samples
Aspirate organic layer
GC/MS Analysis
Data Processing and Results
Extraction #1
with water and ethyl acetate
Edwards S. et al., Clin. Chem., 2012, 58(4), 768-776

## Slide 3
Fresh or Frozen Serum
Transfer serum into UC tubes
Overlay serum with 0.195M NaCl
Ultracentrifugation (UC)
DAY 2: Isolation and Reconstitution of Centrifuged Cholesterol Fraction
DAY 1: Sample Preparation and Ultracentrifugation
Slice UC tube, removing the top layer of CMs & VLDL
Transfer content quantitatively in the UC tube into 5mL volumetric flask
Mix on the rotary mixer
HDLC
Use 0.15M NaCl to fill to the mark
BFC
Transfer 2mL
Transfer remaining (BFC) in storage vials & freeze
Add Heparin
Add MnCl2
Place on ice
Centrifugation
DAY 3: Abell-Kendall Method Analysis
Transfer supernatant in storage vials & freeze
DAY 3: Abell-Kendall Method Analysis
Measure BFC
LDLC = BFC - HDLC
Measure HDLC
HDLC
Supplemental Figure 3S. HDL-C and LDL-C RMP based on ultracentrifugation and Abell Kendall RMP
In: Handbook of Lipoprotein Testing, 2nd Edition. Washington DC: AACC Press 2001: 227-230.

## Slide 4
Fresh, Frozen or
Reconstituted Lyophilized Serum
Gravimetrically add IS, sample/calibrator
Hydrolysis
Sample Extraction
Dry organic layer under nitrogen
Transfer organic layer to a new culture tube
Add Derivatizing reagent and vortex
Place in oven
Data Processing and Results
Add hexane and DI water to perform liquid-liquid extraction
GC/MS Analysis
Add alcoholic KOH solution
Transfer to GC vials
Supplemental Figure S4. Schematic representation of total cholesterol isotope dilution gas chromatography mass Spectrometry (ID GC MS) RMP
Edwards SH, et al Clin. Chem., 2011, 57, 614-622

## Slide 5
Fresh or Frozen Serum
Add IS to each sample/calibrator
Sample Digest
Sample Centrifugation and Transfer
Solid Phase Extraction
Dry Samples Using Nitrogen
Centrifuge the sample plate
Condition and equilibrate the solid phase extraction plate
LC-MRM-MS Analysis
Add LysC and trypsin to digest the sample
Dilute serum samples 20-fold in ammonium bicarbonate
Reconstitute Samples Prior to Analysis
Heat-denature and chemically reduce the sample
Wash solid phase extraction plate and elute off samples
Add sodium deoxycholate and Tris(2-carboxyethylphosphine)
Add to iodoacetamide alkylate the sample
Quench digest with addition of formic acid
in methanol (to precipitate out the deoxycholate)
Transfer supernatant to a clean vessel for solid phase extraction
Data Processing and Results
Denature, Reduce, and Alkylate Sample
Ruhaak LR, et all. Clin. Chem, 69 (3), 2023, 251–261
Supplemental Figure S5. Lp(a) Liquid Chromatography Mass Spectrometry (LC-MS) RMP